UNIVERSITY OF ELDORET

SCHOOL OF EDUCATION

TECHNOLOGY EDUCATION,

ELECTRICAL AND ELECTRONICS TECHNOLOGY

ELT 431 OPERATIONAL AMPLIFIERS CAT  2015/2016

Q1	A double-input, single output differential amplifier is made of identical transistors. It has a 10kΩ collector resistor, 20kΩ tail resistor and two 1kΩ base resistors. A dual power supply of +/-15V is used to power the amplifier. If the transistors have a dc beta of 1000, an emitter to base voltage of 0.7V and an emitter dynamic resistance given by r’e=50mV/IE,

- Sketch the amplifier circuit.

- Determine the amplifier’s tail current.

- Calculate the amplifier’s gain.

- Calculate the amplifier’s output voltage if the input voltages v1 and v2 are 10.4993V and 10.4882V respectively.

- Calculate common mode ratio.

- Calculate common mode rejection ratio.			(20MARKS)

Q2	A 555 timer IC is used to produce 4 kHz clock output at 80% duty cycle. If a 5kΩ discharge resistor is used,

  - Sketch and label the schematic circuit diagram of the clock design.

  - Determine the value of the timing capacitor.

  - Calculate the value of the second timing resistor.	(20MARKS)

Q3	Give a variable three terminal 1.2V-37 /1A and (-) 1.2V-(-) 37V/1A IC regulators and other components to design a power supply that outputs +/- 15V @ 6A, operating from 240V/50Hz;

- Sketch the schematic circuit diagram of the design.

- Calculate the values of all resistors needed for the +/- 15V output.

- Value of the booster current transistor biasing resistor(s).	(20MARKS)

Q4	Design a non-inverting ac op-amp amplifier with a gain of 2-50. Label the values of components.							(20MARKS)

Q5	A ten input DAC outputs 100mV for a digital input of 10102. Calculate the

- Step-size in volts.

- Percent resolution.

- Full-scale output voltage of the DAC.

- The magnitude (value) of the digital input or reference voltage.(20MARKS)