W1-2-60-1-6

JOMO KENYATTA UNIVERSITY

OF

AGRICULTURE AND TECHNOLOGY

University Examinations 2014/2015

END OF SEMESTER EXAMINATION FOR THE DEGREE

OF BACHELOR OF SCIENCE IN CIVIL ENGINEERING

ECE 2207:  ENGINEERING DRAWING III

DATE:  APRIL 2015		  				    	                 TIME: 2 HOURS

INSTRUCTIONS:   	THERE ARE THREE SECTIONS ANSWER ALL QUESTIONS.

ANSWER EACH SECTION ON A SEPARATE DRAWING PAPER

SECTION A (30 Marks)

1. a)	Fig 1(a) show a partial structural steel floor framing.  To a scale of 1:20 make a detailed workshop drawing of the section labeled A and dimension fully.		(20 Marks)

Note:

| 1. |  | Section | Description | Level |
| --- | --- | --- | --- | --- |
|  |  | A | 610WF 101 | 0 |
|  |  | B | 610WF 140 | 0 |
|  |  | C | 305WF 48 | -50 |
|  |  | Clm x (Beam) | 914WF 201 | - |

2.	Use 3 row connections.

3.	ϕ 20 H.S bolts are used.

4.	Beam dims table is provided

b)	Fig 1 (b) shows part of a wooden framework.  Parts A and B are joined using a halving joint and reinforced by us of 2 gauge 20 – 18mm long countersunk head screws.  To a scale of 1:1 draw:

(i)	The front elevation X and

(ii)	The end elevation Y

of the assembled component.	Insert all dimensions.				(10 Marks)

SECTION B

a)	The data shown in the table below has been extracted from a topographical map for a proposed access road in a residential development:

| Existing ground levels (m) | 99.88 | 99.98 | 100.06 | 99.78 | 99.78 |
| --- | --- | --- | --- | --- | --- |
| Formation level (m) | 99.49 | 99.53 | 99.56 | 99.49 | 99.39 |

Given that the levels have been taken at 20m intervals and that the total constructed road thickness is 480mm; prepare an appropriately scaled working drawing for the access road longitudinal profile showing the finished road levels.

[Hint:  Probable scales,or as appropriate]		(10 Marks)

b)	State four functions of a road kerb.						(2 Marks)

c)	Draw a scaled inverted block drain (IBD) assembly given the following engineer’s specification:

*	IBD diameter 300mm

*	100mm thick murram blinding to side slab.

*	600 x 225 x 75mm side slabs provided in two courses.

*	Mortar joint

[HINT:  Probable Scale 1:10]

or as appropriate								(8 Marks)

SECTION C

a)	Using an appropriate scale, draw a rectangular manhole type ‘A’.  Show:

(i)	Two cross-sections							(14 Marks)

(ii)	Plan									(6 Marks)