JOMO KENYATTA UNIVERSITY

AGRICULTURE AND TECHNOLOGY

University Examinations 2014/2015

FIRST SEMESTER EXAMINATION FOR BACHELOR

OF SCIENCE DEGREE IN SOIL, WATER AND ENVIRONMENTAL ENGINEERING

ASE /AAE 2404: SOIL EROSION AND CONTROL /WATER AND SOIL CONSERVATION

DATE:  APRIL 2015		  				    	                            TIME: 2 HOURS

INSTRUCTIONS

- Answer question ONE and any other TWO questions in the booklet provided.

- Use neat sketches where appropriete.

- Observe instructions in the answer booklet

QUESTION ONE (30 MARKS)

- Discuss the role of the THREE main processes of water erosion 		(6 marks).

- Explain how the following factors affect soil erodibility

- Wind affected area                                                           		(2 marks)

- Soil water content							(2 marks)

- Surface roughness                                                       		(2 marks)

- Aggregate stability						 	(2 marks)

- A watershed of 4 km2 receiving an average precipitation of 50mm per day is under three different uses. A third of the watershed consists of agricultural lands with crops planted in straight rows under good condition, half of the watershed consists of residential area with 40% of impervious surface from houses and paved driveways, and the rest of the watershed is under woods with dense litter cover. Table 1 shows the curve numbers for the selected surface conditions for different hydrological groups. Estimate the runoff amount that is produced by the watershed given that the soils are part of the hydrologic group B.			 (6 marks).

Table 1: Runoff curve numbers for selected surface conditions for different soil hydrologic groups (Adapted from USDA-SCS, 1986)

| Surface condition | Hydrologic condition | Hydrologic soil group |
| --- | --- | --- |
|  |  | A | B | D | C |
| Urban Areas |  |  |  |  |  |
| Impervious areas (roofs, streets, parking lots, and driveways |  | 98 | 98 | 98 | 98 |
| Pervious areas (lawns, parks, golfcourses, etc.) | Good | 39 | 61 | 74 | 80 |
| Gravel streets and roads |  | 76 | 85 | 89 | 91 |
| Compacted soil surface (roads and streets and right-of-way) |  | 72 | 82 | 87 | 89 |
| Agricultural Lands |  |  |  |  |  |
| Fallow: Bare soil |  | 77 | 86 | 91 | 94 |
| Fallow: Crop residue cover | Poor | 76 | 85 | 90 | 93 |
|  | Good | 74 | 83 | 88 | 90 |
| Row crops 1. Straight rows | Poor | 72 | 81 | 88 | 91 |
|  | Good | 67 | 78 | 85 | 89 |
| 2. Straight rows + residue cover | Poor | 71 | 80 | 87 | 90 |
|  | Good | 64 | 75 | 82 | 85 |
| 3. Straight rows + contoured terraced + residue cover | Poor | 65 | 73 | 7980 | 81 |
|  | Good | 61 | 70 | 77 | 80 |
| Non-Cultivated Lands |  |  |  |  |  |
| Pasturelands, grasslands, and rangelands | <50% ground cover | 68 | 79 | 86 | 89 |
|  | 50% to 75% cover | 49 | 69 | 79 | 84 |
|  | >75% cover | 39 | 61 | 74 | 80 |
| Woods | Grazed or regularly burned | 45 | 66 | 77 | 83 |
|  | Grazed but not burned | 36 | 60 | 73 | 79 |
|  | Ungrazed | 30 | 55 | 70 | 77 |

- Differentiate  between the following terms as used in soil erosion:

- Gross erosion and sediment yield						(2 marks)

- Tillage erosivity and landscape erosivity					(2 marks)

- Physical factors such as shape, size of a watershed and soil properties influence soil erosion in different ways. Explain how these factors particularly contribute to the occurrence of gully erosion.										(6 marks)

QUESTION TWO (20 MARKS)

- The Universal Soil Loss Equation (USLE) predicts the long term average annual rate of erosion on a field slope based on rainfall pattern, soil type, topography, crop system and management practices. Outline the USLE equation and discuss the functions of each of the five major factors which are used to calculate the soil loss for a given site. 				(5 marks )

- Discuss  tillage erosivity as  a factor that affects tillage erosion			(6 marks)

- Estimate the time of concentration for a 1.5 km2 watershed with soil hydrologic group C that has an overland slope length of 90m with a slope of 4.5%. The channel length is 4 km with a slope of 0.7%. The Manning’s coefficient of roughness for the watershed is 0.17 and that for the channel is 0.011. 									(4 marks).

- Outline FIVE impacts of sedimentation on water resources 				(5 marks)

QUESTION THREE (20 MARKS)

- A survey was carried out in a large watershed to determine soil loss. The watershed was delineated into 6 areas with different land covers and soils as shown in the table 2 and table 3 shows m-values for various slope percentages.

Table 2: Characteristics for the various watershed areas

| Area | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Slope (%) | 2 | 3 | 4 | 4 | 6 | 6.5 |
| Land cover (%) | No appreciable canopy, 20% grass ground cover | 25% tall weeds canopy cover, 40% ground cover (weeds) | 25% tall weeds canopy cover, 60% ground cover (weeds) | 50% canopy of bushes, with 80% ground cover (grass) | 75% canopy of trees, 80% grass cover | 75% canopy of trees, 100% grass cover |
| Type of soil | Alluvial soils | Brown soils | Brown soils | Brown forest soils | Brown forest soils | Reddish-brown soils |
| Slope length (m) | 60 | 30 | 45 | 60 | 25 | 20 |
| Management practices | contouring | contouring | Contour strip cropping | Terracing for erosion control planning | Terracing for prediction of sediment load | Terracing for prediction of sediment load |

Table 3: m-values for various slope percentages

| Slope (%) | ≤ 3 | = 4 | ≥ 5 |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| m-value | 0.3 | 0.4 | 0.5 |  |  |  |

LS = (X/22.1)m (0.065 + 0.045 S + 0.0065S2)………………………Equation 1

Where X = slope length (m) and

S = slope gradient (%)

Given equation 1 above, and the rainfall erosivity is 300,

- Assuming no support system in the area calculate the total soil loss from the catchment obtained using equation 1. 									(3 marks).

- Suppose the farmers in the area decide to carry out various management practices as shown in the table above. Calculate the change in soil loss.					(4 marks).

If only 75% of this soil loss reaches the reservoir downstream, determine the sediment delivery ratio.												 (3 marks).

- List any FOUR application of the USLE equation.	.				 (4 marks)

- Discuss any THREE measures that can be applied to control wind erosion on agricultural lands.

(6 marks)

QUESTION FOUR (20 MARKS)

- Discuss the advantages of using the following measures in the reduction of soil erosion.

- Intercropping								  (2 marks)

- Contour farming							  (2 marks)

- Multi-storey cropping						   (2 marks)

- Differentiate between the following terms:

- Rainfall erosivity and soil erodibility                                                           (2 marks)

- Suspension and saltation                                                                               (2 marks)

- Discuss how the following factors affect time of concentration as an influencing factor of runoff erosivity.

- Surface roughness								(2 marks)

- Watershed slope								(2 marks)

- Length and shape of the channel						(2 marks)

- Explain how the following factors affects tillage erosion

- Landform  erodibility								(2 marks)

- Soil erodibility								(2 marks)

QUESTION FIVE (20 MARKS)

- Not all material removed through soil erosion is transported by the streams into reservoirs. Describe the causes of variations in sediment delivery between watersheds.	(6 marks)

- The rainfall records of a certain catchment are tabulated below.

| Intensity (mm/hr) | Amount (mm) |
| --- | --- |
| 0-25 | 30 |
| 25-50 | 25 |
| 50-75 | 15 |
| >75 | 10 |

Calculate the rainfall erosivity							          (6 marks)

- Outline any TWO activities that may lead to vegetation degradation. 		(2 mks)

- Describe the processes  of  wind  erosion                                                                   (6 mks)

Table 4: K factor value

| Alluvial Soils | 0.15 |
| --- | --- |
| Chestnut Soils | 0.22 |
| Hydromorfic Alluvial Soils | 0.15 |
| Brown Forest Soils | 0.20 |
| Bare Rocks, River Bed etc. | 0.001 |
| Brown Soils | 0.13 |
| Reddish – Brown Soils | 0.04 |
| Kolluvial Soils | 0.18 |
| Noncalcic Brown Forest Soils | 0.29 |

***END***