JARAMOGI OGINGA ODINGA UNIVERSITY OF SCIENCE AND TECHNOLOGY SCHOOL OF SPATIAL PLANNING AND NATURAL RESOURCE MANAGEMENT

UNIVERSITY EXAMINATION FOR DEGREE OF BACHELOR OF SCIENCE IN WATER RESOURCES AND ENVIRONMENTAL MANAGEMENT

2ND  YEAR 2ND   SEMESTER 2016/2017ACADEMIC YEAR

REGULAR

COURSE CODE: PSQ 3115

COURSE TITLE: RESOURCES OF WATER IN TECHNOLOGY

EXAM VENUE: LR 6    		              STREAM: (Water Sciences)

DATE:		    		   EXAM SESSION: 9.00 – 11.00 AM

TIME:  2.00 HOURS

__________________________________________________________________

Instructions:

- Answer  question  1 (Compulsory) and ANY other 2 questions

- Candidates are advised not to write on the question paper.

- Candidates must hand in their answer booklets to the invigilator while in the examination room.

QUESTION ONE

- Explain four factors that you would consider when selecting type of dam to construct?                    											      (8 marks)

- Using energy equation, describe how gross energy head of water in motion contributes to   Hydropower Production  	   			                   		     	      (4 marks)

- Explain four factors that are applicable for purposes of classification of hydro-power plants  										     		     (8 marks)

d) Briefly explain the mechanism of hydropower production                                       	     (4 marks)

e) Explain six components of hydroelectric power system                                                      (6 marks)

QUESTION TWO

- Considering storage required for a uniform demand of a reservoir, sketch a mass inflow curve  from a flow hydrograph for 5 consecutive years (1950 to 1944), and indicate possible positions/ sections:

- Where the reservoir is considered  full and empty

- That determines the demand capacity

- That determines the required storage                   		    		   (8 marks)

- A reservoir has the following areas enclosed by contours at various elevations. Determine the capacity of the reservoir elevations of 300 to 400.

| Elevation | 300 | 320 | 340 | 360 | 380 | 400 |
| --- | --- | --- | --- | --- | --- | --- |
| Area of contours (Km2) | 180 | 205 | 230 | 320 | 400 | 460 |

By:

- Trapezoidal Rule  								    (12 marks)

- Prismoidal Rule

QUESTION THREE

- Explain the three kinds of failures that would prompt you to conduct dam stability analysis

(6 marks)

- A gravity dam might experience disturbances against the expected stability designed for it as illustrated in the diagram below. Cases of occurrence of such forces might reduce design life of the dam or might cause damage to it.

Required:

- Describe the necessary procedure for dam stability analysis  			(10 marks)

- How would you determine if the dam would be safe? 				 (4 marks)

QUESTION FOUR

- With reference to a reservoir and its catchment, explain four factors that Influence/ affect sedimentation and four  methods that can be adopted to control reservoir siltation.          (8 marks)

- Yatta village has a drainage basin area of 40,000 m2. The basin experiences an estimated suspended sediment discharge of 36,000 kg/year and a bed load discharge of 22,000 kg/year.

The estimated bed load density = 2500kg/m3

The estimated soil density = 500kg/m3

Calculate:   (i)    The Erosion rate and Unit Erosion Rate of the reservoir

- The rate at which the bed-load would be lowered

- The Rate at which the soil will be lowered  			    (12 marks)

QUESTION FIVE

- For purposes of solving water needs in a society, explain two functions of a water resource technologist/ engineer  					   			      (2 marks)

- Describe Three  kinds of investigations usually conducted for reservoir planning     	     (6 marks)

- Define the terms Dead Storage and Safe Yield  as used in reservoir engineering               (2 marks)

- A hydrostatic power plant takes in 30m3/s of water through its turbines and discharges it at v = 2m/s at atmospheric pressure. The Head loss in the turbine and conduit system is 20m.

- Using Bernoulli’s energy equation, determine the net energy head, H  in meters

- Estimate the power, P, extracted by the turbine in Watts	               	    (10 marks)

# Text boxes

Earthquake forces

Reservoir

100m

Elevation 50m

Turbine

Elevation 150m

heel

toe

x

Tail water

Rx

Uplift forces

Ø

Ø

crest

Wave pressure

Silt pressure

Base width

Hydrostatic force

W

Ry